## Slide 1
The Future Role of Gas Networks in Integrated Energy Network
Devasanthini Devaraj & Dr Eoin Syron

## Slide 2
Sustainable Development Goal
Affordable, reliable, sustainable & modern energy
Enhance energy research
  Renewables
  Cleaner fossil-fuel technology
Expand and upgrade infrastructure
Why do we care?
What can we do?

## Slide 3
Ireland’s Energy Balance
3.6%
23%
Notes: Where are we today?
Where we could go?
How do we get there?

## Slide 4
Overview of Irish Gas Network
14,712 km of pipelines
Entry points to Irish gas system
  Corrib, Inch and Moffat
30% of the total energy mix
  Half of the Electricity Generation
Chart: TPER Analysis by Fuel
| Gas | Oil | RES | Coal | Peat
 | 0.298 | 0.48 | 0.093 | 0.076 | 0.048
Chart: Electricity Generation by Fuel, 2017
| Gas | Coal | Wind | Peat | Other RES | Hydro | Oil
 | 0.51 | 0.183 | 0.135 | 0.103 | 0.05 | 0.013 | 0.008
Notes: What is the Gas Network & what does it do today
How much energy is transported per day
Where is it coming from % break down
How much CO2 is it emitting today
Sources
https://www.seai.ie/publications/Energy-in-Ireland-2018.pdf
Notes
GNI transported 74,000 GWh of energy in 2017.
Electricity generation via natural gas was 367 gCO2/kWh in 2015, whereas it was 907 gCO2/kWh and 1059 gCO2/kWh for coal and peat respectively.
Irish gas network consists of 2427 km of high-pressure steel transmission pipelines which operates above 16 barg.
It consists of 11527 km of low-pressure polyethylene distribution pipelines which operate at 4 barg.
Content

## Slide 5
Capacity of Gas Network
Asset Value | €2.8 bn
Energy Transported | 175 GWh/day
Energy Stored | 
Pipe diameter | 15 inches
Length | 1 km
@70 barg | 310 MWh
@80 barg | ↑13%
@90 barg | ↑28%
Notes: How much did it cost?
How much energy can it store/ hold?
@70Barg
@80Barg
@90Barg
Sources
https://www.ervia.ie/ervia-annual-report/GNI-Group-Financial-Statements-2017-V3.4-with-Audit-scaled-and-signatures-.pdf
Content

## Slide 6
Comparison with Electric Network
Transporting gas by pipeline is cheaper
  2/3rd cheaper than electricity (€ per km per kW)
Gas pipelines are less expensive to build than electric transmission lines
  50 - 60% of the cost of electric lines
Notes: Limitations of Electrical Network and storage
Comparison cost
https://pubs.rsc.org/en/content/articlelanding/2018/ee/c7ee01987d#!divAbstract
http://www.northwestchptap.org/nwchpdocs/transmission_and_n_gas_comparing_pipes_and_wires_032304.pdf
Notes
Maximum cost ($ per km per kW) to transport gas is 0.16
Minimum cost to transport electricity is 0.48
Gas costs at least 2/3rd lesser than electricity
Content

## Slide 7
Comparison of Energy Storage Technologies
Notes: Content

## Slide 8
Gas Network in the Future Energy System
  Cheaper
  FSRU
  Substitute for pipeline imports
LNG
  Energy storage
  Limitations to be used in existing network
  Gas quality
Hydrogen
  Injected into gas network
  Compatible with gas appliances
  BioCat
Synthetic Natural Gas (SNG)
  Used in SNG production
  Can be transported in pipelines
CO2
  Gas storage in pipelines by increasing pressure
Line pack
Notes: What could it be used for in the future
Hydrogen transport
European projects
Content

## Slide 9
Hydrogen
sample image

## Slide 10
Role of Gas Network
NATURAL GAS / MIXED GAS NETWORK
Biomethane Injection
Pipeline/LNG Imports
CNG Refuelling
Hydrogen Storage
Methanation
Cogeneration/CHP
Carbon Capture
Methane Reforming
Power Generation
Electrolysis
Gas
Hydrogen
CO2
Heating
Gas Extraction

## Slide 11
Gas Network Developments
  Compressed Natural Gas (CNG) refuelling network
  Renewable gas injection
  CNG Vehicle fund
The CAUSEWAY Project
  Convert gas network to 100% H2 (techno-economic feasibility)
  City of Cork to H2
H21 Leeds
  Dependency on gas-fired power plants
  CO2 storage in Kinsale (local gas network for CO2 transport)
  Steam Methane Reforming + CCS
Carbon Capture & Storage (CCS)
Notes: Sources
https://www.gasnetworks.ie/business/natural-gas-in-transport/the-causeway-project/
https://www.cru.ie/wp-content/uploads/2018/12/CRU18269a-GNI-Network-Development-Plan-2018.pdf
Content:

## Slide 12
Outlook for the future Gas Network:
Storage (Underground, LNG)
Transport infrastructure
Support for renewable energy sources
Immediate substantial reduction in CO2 emissions
Hydrogen network
Recognise Decarbonisation
Existential Crisis
Change in business
100% Electrification?
Less clarity or Uncertainty
Route to decarbonisation
Network fragmentation?
Pilot projects
Lack of consensus
Cost and commerciality
Stake holders and Consumers
Technical Issues
Gas quality
Certification
key issues for discussion

## Slide 13
Modelling of Gas Network
P2G settings
5 MW
40 MW
120 MW
150 MW
200 MW

## Slide 14
End use of gas towards a zero-emission future
Will gas be used for Renewable Energy Storage?
Will gas continued to be used in the Heating Sector?
Will gas continued to be used for Power Generation?

## Slide 15
Storage tanks
Regas unit
Future Role of Gas Networks
  Diversification of gas sources (LNG)
  De-fossilization of gas network (SNG)
  Future of gas network
Overview
  FSRU for long-term LNG storage
  Quantify Boil-off Rate and Wobbe Index
  Economic Analysis
Incorporation of LNG via FSRU
  Multiple process flow configurations in SNG production
  Factorial design + ANOVA  maximum profit generated by SNG
Synthetic Natural Gas Production
Notes:   Diversification of gas sources
  Increasing gas demand
  Growth in LNG trade globally
  Investigate the possibility of FSRU as a long-term LNG storage facility
  Perform simulation to quantify boil-off rate and wobbe index of LNG during storage
  Case Study: Ireland
  LNG after 10 weeks of storage is suitable to inject into gas network
  Price per unit of regasified LNG is 42% lower, substitute for pipeline imports
  De-fossilization
  Directly injected into gas network
  Support the variability of renewables
  Multiple process flow configurations in SNG production
  Factorial design + ANOVA  maximum profit generated by SNG
  Most influential variables - Methanator capacity, Electrolyser capacity & Electrolyser efficiency
  Optimal configuration - Biogas upgrader as the CO2 source and H2 from the electrolyser
  Maximum profit -10 cent/kWh of SNG
  Content

## Slide 16
References
1 | https://www.seai.ie/publications/Energy-in-Ireland-2018.pdf
2 | https://www.ervia.ie/ervia-annual-report/GNI-Group-Financial-Statements-2017-V3.4-with-Audit-scaled-and-signatures-.pdf
3 | A capital cost analysis of energy transmission via natural gas pipelines and overhead electric wire lines: A Joint Study by the Bonneville Power Administration and the Northwest Gas Association
4 | Saadi, Fadl H. and Lewis, Nathan S. and McFarland, Eric W. (2018), “Relative costs of transporting electrical and chemical energy”. In: Journal of Energy Environ. Sci.
5 | https://www.gasnetworks.ie/business/natural-gas-in-transport/the-causeway-project/
6 | https://www.cru.ie/wp-content/uploads/2018/12/CRU18269a-GNI-Network-Development-Plan-2018.pdf
7 | https://www.gasnetworks.ie/corporate/gas-regulation/system-operator/publications/Long-Term-Resilience-Study-2018.pdf

## Slide 17
Thank you
Funded by