## Slide 1
Deep Electrification of Residential Heating and Possible Implications
DATE
17th September 2019
VENUE
ESRI, Whitaker Square, Dublin
AUTHORS
Ankita Singh Gaur
Desta Fitiwi
John Curtis
Muireann Lynch

## Slide 2
Acknowledgements
This work has emanated from research conducted with the financial support of Science Foundation Ireland under the SFI Strategic Partnership Programme Grant Number SFI/15/SPP/E3125. The opinions, findings and conclusions or recommendations expressed in this material are those of the author(s) and do not necessarily reflect the views of the Science Foundation Ireland.

## Slide 3
Motivation
Objectives
Methodology
Assumptions and Scenarios
Results
Conclusion
Outline

## Slide 4
Motivation
The residential sector accounts for a quarter of the energy used in Ireland
It is responsible for a quarter of the energy-related CO2 emissions.
Chart: Residential Energy Demand
| Space Heating | Lighting and appliances | Cooking | Water heating
Sales | 61 | 17 | 3 | 19
Source: SEAI, 2018

## Slide 5
Motivation
Chart: Space Heating (Fuel type)
| Electricity | Gas | Solid Fuels | Oil | Renewables
Space Heating | 67 | 405 | 347 | 780 | 53
In Ireland, domestic space heating was responsible for about 10 MtCO2 emissions in 2016 (17% of the total emissions)
Source: SEAI, 2018

## Slide 6
Power-to-heat (P2H) with a thermal storage is a promising solution that helps countries such as Ireland to fulfil environmental goals
However, a higher penetration level of P2H could mean a dramatic increase in electricity demand, with this having implications on the existing grid infrastructures
Motivation
Notes: The new climate action plan released two weeks back mentions a target of installing 600,000 heat pumps in Ireland by 2030. 400,000 from retrofits and 200,000 from new builds.

## Slide 7
Develop an optimization framework that enables understanding the interactions between the power and the heating sectors for the Irish transmission grid
Provide a quantitative as well as qualitative analysis on the impacts of P2H (Air Source Heat Pumps) in terms of grid and power generation expansion needs as well as overall system performance
Objectives

## Slide 8
The Electricity Network and Generation INvEstment (ENGINE) model is used
Determines the least-cost development of power systems in Ireland and beyond.
Methodology
Outputs
Development
Inputs
Methodology
Developed in ESRI
Electricity Network & Generation INvEstment Model
Linearised AC optimal power flow model
Least cost optimization
Stochastic programming framework
Coded in GAMS
Policy Measure
Uncertainty & Variability
Technology & demand data
Network & generation data
Heat sector data
Optimal power generation mix
Grid expansion outcomes
Impact analysis
Comparative analysis
Interaction of flexibility options
ENGINE

## Slide 9
Methodology
ENGINE
E-Heat Model
Heat demand balance
Thermal losses
Thermal energy storage balance
Other Constraints
  Capacity of heat pump
  Limits on storage levels
  Charge/discharge limits of storage
Integrated Power system and E-heat model
Electrification of heat demand via heat pumps will increase the overall demand for electricity, challenging the existing power system infrastructure
The aim is to obtain a least-cost transmission system when the heat demand is electrified

## Slide 10
Case-1: Impact of electrifying new housing developments
Case-2: Impact of retrofitting old housing stock
Case Studies

## Slide 11
Case-1

## Slide 12
The transmission system consists of 676 supply and demand points connected by 900 transmission lines and transformers
Heat pump (HP) capacity- 1.504 kW, Thermal energy storage (TES) capacity- 50 kWh
Heat pumps are installed in new, well insulated buildings and housing developments
Assumptions and Scenarios

## Slide 13
The analysis in this work considers 3 cases designated as:
Business as Usual (BaU)
Direct E-Heating
E-Heating with TES
Assumptions and Scenarios
Direct E-Heating
E-Heating with TES

## Slide 14
In line with EirGrid’s projections, two e-heating demand growth scenarios are simulated, “Low E-Heating Scenario” & “High E-Heating Scenario”
Assumptions and Scenarios
Chart: Annual Heat Pump Demand Projection
| 2015 | 2020 | 2025 | 2030
Low E-Heating | 0 | 0.2 | 0.2 | 0.4
High E-Heating | 0 | 0.3 | 0.8 | 1.2
Chart: Dwellings with heat pumps
| 2020 | 2025 | 2030
Low E-Heating | 2.4823 | 2.5773 | 4.8576
High E-Heating | 3.3688 | 10.3093 | 14.0704

## Slide 15
Results
Chart: Transmission Capacity Expansion needs in 2030
| BaU | Direct E-heating | E-heating with TES
HDG_2
HDG_6
Low E-heating Scenario | 0 | 2.509 | 0.58751
High E-heating Scenario | 0 | 5.3387 | 4.3418
Additional electricity transmission capacity is required with HP penetration; however, using TES can reduce this requirement
Notes: With the “Direct E-Heating” case in the “Low E-Heating” scenario, it can be observed that partly electrifying the heat demand increases transmission expansion requirements by 2.5% compared to that of the BaU scenario. However, if this is done along with thermal energy storage, compared to that of the BaU case, the network needs to only be expended by 0.58%, expressed in terms of additional transmission line capacities in the system. A similar trend can be observed in the “High E-Heating” scenario in which the “Direct E-Heating” case requires 5.3% more transmission capacity than in the BaU scenario, while in the “E-Heating with TES” case requires 4.3% new transmission capacity in the system. This explains the advantages of installing heat pumps along with thermal energy storage devices to reduce the transmission capacity needs.

## Slide 16
Results
Heat pumps enable a more efficient utilization of variable renewable power
Chart: Renewable Power Utilization in 2030
| BaU | Direct E-heating | E-heating with TES
Wind-2
Solar-2
Hydro-2
Biomass-2
Total-2
Wind-6
Solar-6
Hydro-6
Biomass-6
Total-6



## Slide 17
Results
Chart: Emissions in 2030
| BaU | Direct E-heating | E-heating with TES
HDG_2
HDG_6
Low E-heating Scenario | 0 | 0.58324 | 0.10103
High E-heating Scenario | 0 | 1.7862 | 0.34063
Heat pumps cause additional power generation, and hence there is an increase in emissions
With TES the emissions are lower due to load shifting

## Slide 18
Results
Chart: Relationship between wind generation & TES charge/discharge cycle
Excess variable renewable energy (mainly wind) is stored during low-demand periods, and released when the heat demand is high and the wind energy is not available

## Slide 19
Case-2

## Slide 20
Heat demand consists of 2 parts:
heat demand arising from new builds using heat pumps for domestic heating
heat demand from old houses retrofitted by 2030
Data on existing housing stock is taken from the Central Statistics Office (CSO), Ireland (2016 Census data)
The analysis considers two scenarios for nine different values of thermal heating costs (THC)
As thermal heating costs rise, electrification of heat increases, which increases demands on the power system
Assumptions and Scenarios

## Slide 21
Results
Chart: Optimal electrification level
| 20 | 30 | 40 | 50 | 60 | 70 | 80 | 150 | 200
Direct | 14.2112 | 14.2112 | 14.2112 | 14.2112 | 15.8263 | 21.2885 | 26.3947 | 87.5445 | 95
With TES | 14.2112 | 19.9713 | 66.1111 | 100 | 100 | 100 | 100 | 100 | 100
It is far more economical to electrify residential heating when using TES as compared to the “Direct” case
Notes: In the ”direct” scenario, changes in the penetration level of e-heating are not significant for a penalty factor setting of 80 e/MWh or lower. Only beyond this threshold does the adoption of e-heating make more economic sense. Whereas, when thermal storage systems are deployed as in the second scenario, the
percentage of demand met via e-heating increases significantly from 40 e/MWh onwards. This implies that it is far more economical to electrify residential heating when using TES as compared to the other case. Such a dramatic difference between the two scenarios is explained by the fact that the peak electrical and heating demands mostly happen during the same time periods. Hence, serving the heat demand becomes exorbitantly expensive in the ”direct” scenario. But with TES, excess RES energy (that would otherwise be curtailed as in the ”direct” scenario) is stored during periods of low heat and electrical demand and released during high demand and low RES power production periods.

## Slide 22
Regional distribution of optimally electrified houses
THC =80 (€/MWh); Direct
THC =200 (€/MWh); Direct
THC=30 (€/MWh); With TES
THC=80 (€/MWh); With TES
Notes: the regional distribution of electrified houses is largely determined by the location of wind energy potential and network constraints. This is particularly
relevant in the case of ”direct” scenario. The results generally reveal that the co-deployment of TES leads to a substantially reduced network stress and enhanced system-wide flexibility, the combination of which enables a higher penetration level of e-heating throughout the island.

## Slide 23
Results
Chart: Increase in network expansion needs (expressed as a percent of existing capacity)
| 20 | 30 | 40 | 50 | 60 | 70 | 80 | 150 | 200
Direct | 7.51 | 7.51 | 7.51 | 7.51 | 7.52 | 7.68 | 7.9 | 9.27 | 10.28
With TES | 7.2 | 7.25 | 8.03 | 9.325 | 9.327 | 9.327 | 9.327 | 9.327 | 9.327
Grid reinforcement needs is lower with TES
Notes: At low levels of thermal heating costs, the expansions are similar since there are no investments in retrofits. At medium levels, there is investment only in TES case, hence there is higher expansion need. It is more economical. Also, the grid expansion is only slightly higher although electrification levels are higher. At higher levels of thc, higher electrification and hence higher capacity needed.

## Slide 24
Results
Chart: Wind energy curtailment
| 20 | 30 | 40 | 50 | 60 | 70 | 80 | 150 | 200
Direct | 19.0827 | 19.0827 | 19.0827 | 19.0827 | 18.853 | 18.1085 | 17.4216 | 10.2313 | 9.0517
With TES | 20.5836 | 16.1816 | 5.3828 | 1.5129 | 1.5106 | 1.5106 | 1.5106 | 1.5106 | 1.5106
Wind energy curtailment is substantially reduced with TES, leading to a more efficient utilization of available clean energy sources

## Slide 25
Electrifying the heating sector considerably increases grid expansion needs in the system.
However, the impact highly depends on the growth of heat demand, and the extent of heating sector electrification
Electrification of heating sector enables a more efficient utilisation of variable renewable power, reducing variable power curtailments
It is deemed economical to electrify more houses located near RES-rich places
TES plays a major role in heat sector electrification by:
  Reducing grid investment needs
  Reducing RES curtailment
  Enabling higher electrification at lower PFs
Conclusions

## Slide 26
Questions?
Thank You